## Slide 1
VNM PEDALS LITE
Quick Guide
Box Includes
5
6
1. VNM Throttle
2. VNM Brake
3. VNM Clutch (*)
4. VNM Controller Box
5. USB Cable
6. Allen key set & Mounting screws
7. Red & Yellow springs
Connection
1
2
4
3
Left side: GX12 Ports for:
1. Handbrake 3. Brake
2. Throttle 4. Clutch
Plug each pedal in its corresponding port
Right side:
5. DFU/RUN Mode Switch
Up: DFU Mode
Down: RUN Mode
6. USB Port for PC connection
Pedal Adjustment
7
1. Adjust the height of the Pedal face
3. Adjust the Pedal Stiffness
Move the pivot point of the spring assembly up/down for a stiffer/softer pedal actuation
2. Adjust the Pedal tilt angle
2 height levels at the front and 4 height levels at the back allow multiple tilt angle options
Remove the 2 hex bolts on each side, tilt the pedal to a suitable angle, insert the bolts back into place and tighten them with the hex bolts.
5
6
1
2
3
4
5
6
Loosen the 4 the hex bolts on the sides behind the pedal face, choose a suitable pedal height, then tighten.
1
2
3
4
Twist the spring preload cap clockwise for a stiffer pedal actuation
Or anti-clockwise for a softer pedal actuation
(*) Not included with VNM Lite Pedal set 2

## Slide 2
Step 1: Remove the elastomer stack
Step 2: Choose a suitable combination of springs and elastomers
Option 1: Medium initial travel, medium stiffness
Option 2: Light initial travel, medium stiffness
Option 3: Low stiffness, longer travel
Combinations of 3 elastomers/springs are recommended. Feel free to get creative with different combos.
Step 3: Re-install the elastomer stack
4. Adjust the Pedal travel range
Loosen the 2 hex bolts on the sides, adjust 2 blue bump stops to change pedal stroke
5. Adjust the Brake pedal
Top Bump stop:
Determines the pedal travel end point
Bottom Bump stop:
Determines the pedal travel start point
Adjusting the Top Bump stop
Step 1: Disassemble the spring assembly.
Step 2: Loosen the 4 hex bolts at the (1) & (2) positions on the sides, choose a suitable position for the blue bump stop, then tighten the bolts at the (2) position
Step 3: Move the locating pin to press against the hex bolt (2) then tighten the hex bolt (1) (Applicable with VNM Throttle and VNM Clutch).
Step 4: Reinstall the spring assembly.
Remove the bolts on both sides then remove the spring assembly
min
max
min
max
1
2
1
2
Reinstall the stack and adjust the preload to your liking.
Unlock a wider range of customizability with the VNM Brake Upgrade Kit. This allows you to set various stiffness levels to suit different racing disciplines and
Some possible combinations:
And many more possible combinations
Step 4: Recalibrate in the VNM Configurator

## Slide 3
Throttle Dimensions
Brake Dimensions
Clutch Dimensions
Controller Box Dimensions